IN  THE  NAME  OF  ALLAH

ADDEENDUM NO.1

TERMS AND CONDITIONS OF  ONE  STEP INTERNATIONAL   TENDER  FOR PURCHASE OF 2×35000 MTS %±5 GSOP

GENERAL TERMS  AND  CONDITIONS :

A) ITEM 1-2  SHOULD BE READ :

"OFFERS  WITH  SHIPMENT  BY VSL  SHOULD BE  ON THE BASIS OF FOB , DDP(ONLY FOR IRANIAN SUPPLIER) OR CFR FO BANDAR ABBAS, BIK,BANDAR CHABAHAR, PREFERABLY BY IRANIAN  VSL.

NOTE: IN CASE OF SHIPMENT BY NON–IRANIAN VSL, PAYMENT OF FOREIGN FLAG CHARGES (10 PCT OF TOTAL FREIGHT COST) SHOULD BE ON SELLER'S ACCOUNT ."

B) ITEM NO. 3 SHOULD BE READ:

" TECHNICAL SPECIFICATION BASED ON INSO128 SECOND VERSION 2016 IS AS FOLLOWS INSTEAD OF WHAT MENTIONED BEFORE.

GRANULAR  POTASSIUM  SULPHATE

K2O                                                 	 MIN  50   PCT

MOISTURE                                    	 MAX  1.5 PCT

MgO			                         MAX  2   PCT

Ca (CaO)                                             MAX   2.5 PCT

SULPHATE SOLUBLE IN WATER (S)    MIN 17.5 PCT

NA(NACL)                           	           MAX   2   PCT

GRANULAR  SIZE

BETWEEN 1-4 MM       	                      MIN   85 PCT

NOTE: ANALYSIS METHOD  MUST BE AS PER IRAN NATIONAL STANDARD NO INSO 128 FOURTH  VERSION 2016. CONFIRMED BY SOIL & WATER RESEARCH INSTITUTE."

C: ITEM NO.4 SHOULD BE READ :

PACKING  :

"BIDDERS CAN SUBMIT OFFERS IN BULK OR BAGGED IN 9 AND/ OR 50 KG AS FOLLOWS:

IN CASE OF BAGGED CARGO, THE SPECIFICATION IS AS FOLLOWS: PACKING IN NEW TWO-LAYER PP/PE BAGS. EACH BAG  TO HOLD 9 KGS AND/ OR 50 KGS  NET OF A/M  CARGO, TARE WEIGHT OF EACH BAG TO BE 50± 2 GRAMS AND/ OR 153± 2 GRAMS. BAGS TO BE STANDARD, STRONG ENOUGH AND SUITABLE TO AVOID POSSIBLE DAMAGE. DIMENSION OF THE SEWN UP BAGS SHOULD BE 35 × 50 AND /OR 60 ×90  CM."

.

NOTE 1: ASSC ' LOGO AND TECHNICAL SPECIFICATIONS SHOULD BE SPECIFIED IN ONE SIDE OF EACH BAG IN ENGLISH/PERSION.

NOTE 2:THE BAGGED CARGO SHOULD BE OFFERED ALONG WITH 2PCT SPARE  FREE EMPTY  BAGS OF TOTAL CARGO .

NOTE 3: IN CASE OF 9 KGS BAGGED, THE BAGGED CARGO SHOULD BE OFFERED IN JUMBO BAGS ALONG WITH 2PCT  SPARE  FREE EMPTY JUMBO BAGS OF TOTAL CARGO

AGRICULTURAL SUPPORT SERVICES COMPANY